## Slide 1: First Look AT RENU2 PMT DATA
James Hecht
SSAL
The Aerospace Corporation

## Slide 2
Overview:
Measure Zenith Brightness of 3 auroral features.
  391.4 nm - N2+ Resonance scattering
      Significant emission above 350 km
      N2, O, and electron densities, electron and solar flux
  630.0 nm - electron flux +O (lifetime ~110 s)
      Significant emission above 350 km
      Stronger background
  557.7 nm – electron flux+O (above 250 km), N2+O (lifetime ~ 1 s)
      O, N2
O/N2 ratio
  Need auxiliary Rocket and Radar Data
Point of Contact: James Hecht
Aerospace Photometer Experiment
Description:
3 Filters bandpasses to isolate auroral features
Sunshades to eliminate unwanted solar photons
Angle Power Exiting (Watts)
50 1.9e-10
55 2.6e-12
65 1.9e-12
70 9.1e-13
Fiber Optic Cables transmit photons from Sunshades
3 PMTs to measure photons
PMTS in Aluminum Block
  Block Cooled by LN2 on ground
  Thermal Mass keeps PMTs cool during flight

## Slide 3
Emission Lifetime (tau) then N(t)=N(0)exp(-t/tau)
  Examples for tau of 100 s (1 Rayleigh is 10^6 ph/cm2-s)
    Excitation lasts 1 s
      During first second only 1% emit
        So brightness in Rayleighs is reduced by 100
      In 100 s about (e-1)/e emit
    Excitation lasts 100 s or longer
      During first second only 1% emit
      After about 100 s steady state is achieved
        Brightness in Rayleighs not reduced
  Strickland Models – emissions seen by uplooking PMTs
  AURIC- calculates dayglow emissions
    Altitude, location, time of day, model atmosphere
      Scott Evans of CPI
  B3C electron transport model - calculates auroral emissions
    Altitude, location, time of day, model atmosphere, input electron spectra
      Aerospace
      Model Inputs can include EPLAS and/or Radar Data
      Comparisons can be to Radar, Rocket PMT, or Ground-Based MSP/Imager
ANALYSIS

## Slide 4: EPLAS DATA
As Supplied by Bruce Fritz in May 2016
Data are in ergs/cm2-s-sr
  I multiplied by Pi to convert to ergs/cm2-s (Strickland model Analysis)
    Divided by 18 for these results
    Re-analysis will be needed when updated EPLAS results available
    Probably could use actual pitch angle distribution

## Slide 18
If 1 sec fluctuation then 6300 is reduced by about a factor of 110 compared to 5577
But 6300/5577 model is about 30
So 5577/6300 should be about 4
  Measured 5577/6300 is about 4 to 5
  Implies short time scale
In addition 6300 is reduced by a factor of about 1000 implies about 0.1 to 0.2 s
5577 is reduced by about a factor of 10 implies about 0.1 s fluctuation
6300/5577